## Slide 1: Hash Chain: a Scalable Content Provenance and Integrity Verifying Protocol for NDN
ETRI
박세형 (labry@etri.re.kr)
신용윤 (uni2u@etri.re.kr) August 26, 2020

## Slide 2: Problem Definition
The modern server usually has two CPU sockets on its motherboard. These CPUs usually start at 4 cores and go, as of 2015 for Intel Xeon, up to 18 cores per CPU. While 4-socket and larger servers exist, they are less common today. A two-socket server with 36 cores is an insane overkill for most applications as of 2015. – from Quora
Hash Chain can only utilize one core which is could lead to poor performance even compared to RSA-with-SHA256.
Notes: Batch Chain vs Real-time chain

## Slide 3: Hash Chain light-weight per-packet authentication
Hash Chain (HC) has two mechanisms.
  Batch Hash Chain: This is the default mode that guarantee the provenance upon receiving the packet. However, the provider needs to have the entire sequences before generating hash chain signatures.
  Real-time Hash Chain: This is apt for real-time usage. However, this cannot guarantee the provenance until it receives the last packet. For example, traffic signal of vehicular networks, other real-time tactile IoT signals
Notes: Batch Chain vs Real-time chain

## Slide 4: Forward Chain Signature Generation Example
S2
S1
S3
S4
/example/data/001
/example/data/002
/example/data/003
/example/data/004
S4
/example/data/004
K4 = H(name4 || data4 || 0x0000)
Null_hash = H(0x00000000000000000000000)
Provider
Consumer
S3
/example/data/003
K3 = H(name3 || data3 || k4)
k4 = 0x66970e0d57360fdd4835c80
Notes: 처음에는 10MB 데이터가 있다고 가정… 이를 세그멘트로 8129로 만듬.
그리고 뒤에 있는 세그먼트부터

## Slide 5: Forward Chain Signature Generation Example
S2
/example/data/002
K2 = H(name2 || data2 || k3)
S1
/example/data/001
K1 = H(name1 || data1 || k2)
S2
S1
S3
S4
/example/data/001
/example/data/002
/example/data/003
/example/data/004
Provider
Consumer

## Slide 6: Forward Chain Signature Generation Example
0-step m1 = name1 + data1
(BC-1) kn = H(mn || null_hash)
(BC-2) ki = H(mi || ki+1), all n > i > 1
(BC-3) k1 = H(m1 || k2)
(BC-4) RSA_SIGN(PRCP, K1)
(BC-5) S = E(PRCP , K1, Kn)

## Slide 7
PIT
PIT
PIT
PIT
PIT
PIT
PIT
PIT
m1||k2||s
I(m1)
I(m1)
I(m1)
m1||k2||s
m1||k2||s
I(mi)
I(mi)
I(mi)
mi||ki+1
mi||ki+1
mi||ki+1
CC
CC
CC
CC
CP
CP
CP
CP
Propagation of Interest and Data packets for the Forward Hash Chain

## Slide 8
PIT
PIT
PIT
PIT
I(mn)
I(mn)
I(mn)
mi||kn
mi||kn
mi||kn
CC
CC
CP
CP
Propagation of Interest and Data packets for the Forward Hash Chain

## Slide 9: Forward Chain Signature Verification Example
S1
/example/data/001
K1 = H(name1 || data1 || k2)
S2
/example/data/002
K2 = H(name2 || data2 || k3)
If K2 == K2’: pass
K4, K1 = Decrypt(PUBCP, S)
If K1 == K1’ : pass
※ K1’ prime means calculated
S2
S1
S3
S4
/example/data/001
/example/data/002
/example/data/003
/example/data/004
Provider
Consumer

## Slide 10: Forward Chain Signature Verification Example
S3
/example/data/003
K1 = H(name3 || data3 || k4)
S4
/example/data/004
K4 = H(name4 || data4 || null_hash)
If K4 == K4’: pass
If K3 == K3’ : pass
S2
S1
S3
S4
/example/data/001
/example/data/002
/example/data/003
/example/data/004
Provider
Consumer

## Slide 12: Backward Chain Signature Generation Example
S2
S1
S3
S4
/example/data/001
/example/data/002
/example/data/003
/example/data/004
S4
/example/data/004
K4 = H(name4 || data4 || 0x0000)
Null_hash = H(0x00000000000000000000000)
Provider
Consumer
S1
/example/data/001
K1 = H(name1 || data1 || k4)
k4 = 0x66970e0d57360fdd4835c80
Notes: 처음에는 10MB 데이터가 있다고 가정… 이를 세그멘트로 8129로 만듬.
그리고 뒤에 있는 세그먼트부터

## Slide 13: Backward Chain Signature Generation Example
S2
S1
S3
S4
/example/data/001
/example/data/002
/example/data/003
/example/data/004
S2
/example/data/002
K2 = H(name2 || data2 || k1)
S3
/example/data/003
K3 = H(name3 || data3 || k2)

## Slide 14: Backward Chain Signature Generation Example
0-step m1 = name1 + data1
(BC-1) kn = H(mn || null_hash)
(BC-2) k1 = H(m1 || kn)
(BC-3) RSA_SIGN(PRCP, K1) -> maybe required to hash one more time
(BC-4) ki = H(mi || ki-1), all n > i > 1
(BC-5) S = E(PRCP , Kn, Kn-1)

## Slide 15
PIT
PIT
PIT
PIT
PIT
PIT
PIT
PIT
m1||k1||s
I(m1)
I(m1)
I(m1)
m1||k1||s
m1||k1||s
I(mi)
I(mi)
I(mi)
mi||ki
mi||ki
mi||ki
CC
CC
CC
CC
CP
CP
CP
CP
Propagation of Interest and Data packets for the Batch Hash Chain

## Slide 16: Backward Chain Signature Verification Example
/example/data/001
/example/data/002
/example/data/003
/example/data/004
S1
/example/data/001
S2
S1
S3
S4
K1 = H(name1 || data1 || k4)
S2
/example/data/002
K2 = H(name2 || data2 || k1)
If K2 == K2’: delayed
Provider
Consumer
K4 = Decrypt(PUBCP, S)
If K1 == K1’ : pass
※ K1’ prime means calculated

## Slide 17: Backward Chain Signature Verification Example
S3
/example/data/003
K1 = H(name3 || data3 || k2)
S4
/example/data/004
K4 = H(name4 || data4 || null_hash)
If K4 == K4’: pass
If K3 == K3’ : pass
/example/data/001
/example/data/002
/example/data/003
/example/data/004
S2
S1
S3
S4
Provider
Consumer

## Slide 18
Value | Reference | Description
0 | DigestSha256 | Integrity protection using SHA-256 digest
1 | SignatureSha256WithRsa | Integrity and provenance protection using RSA signature over a SHA-256 digest
3 | SignatureSha256WithEcdsa | Integrity and provenance protection using an ECDSA signature over a SHA-256 digest
4 | SignatureHmacWithSha256 | Integrity and provenance protection using SHA256 hash-based message authentication codes
5 | SignatureSha256WithHashChain | Integrity and provenance protection using HashChain signature over a BLAKE3 digest
6 | DigestBlake3 | Integrity protection using Blake-3 digest
7 | SignatureBlake3WithHashChain | Integrity and provenance protection using HashChain signature over a BLAKE3 digest
2,5-200 |  | reserved for future assignments
>200 |  | unassigned

## Slide 19: BLAKE-3
BLAKE-3 is compatible with SHA-256
  https://github.com/BLAKE3-team/BLAKE3
  https://github.com/BLAKE3-team/BLAKE3/tree/master/c
  BLAKE3 is based on an optimized instance of the established hash function BLAKE2 and on the original Bao tree mode. The specifications and design rationale are available in the BLAKE3 paper. The default output size is 256 bits. The current version of Bao implements verified streaming with BLAKE3.

## Slide 20: Implementation
https://named-data.net/doc/NDN-packet-spec/current/signature.html
Ndn-cxx HashChain
ndn-cxx/ndn-cxx/security/
  Along with signature-sha256-with-ecds
  Digest-sha256
  Digest-blake3
  Signature-hash-chain-with-blake3
Validation-policy and key-chain:
  Make changes to validate hash chain
  Make changes to validate Blake3
Notes: 어플리케이션에서 멀클해시트리를 사용해도… N개의 RSA 싸인이 필요하다.

## Slide 21: Conclusion
Let’s discuss!
How to embed a Signature and keys
  Signature in the data
  (Data – size of signature)
  Keys are placed as same as DigestSha256
  https://named-data.net/doc/ndn-cxx/current/doxygen/d4/d08/sha256_8cpp_source.html